|  | ......................... pcs. .............................. € .............................. € GEZE Slimline fanlight opener OL 90 N For daily aeration and ventilation on vertically installed semicircular arch or segmental arch bottom-hung casements, inward opening. actuation with electric linear drive E 212 Installation can be carried out from the front, without visible attachment screws. Casement is fitted with safety catch and locking device in the scissors. Casement closing pressure must be adjusted at the casement bracket. Variable stroke adjustment for simple regulation of the opening width For window cleaning, the scissors can be disengaged quickly by pressing the release catch. With flexible rods. Technical data: Opening width: 170mm Leaf width: ........ mm ( ) 1 scissors for casement widths from 500 - 1300 mm1) ( ) 2 scissors for casement widths from 1300 - 2400 mm1) 1) Heed panel widths Casement height: ........ mm (min. 300 mm) Centre of scissors to lower edge Hand lever base plate: ........ mm Colour: ( ) silver-coloured ( ) dark bronze ( ) white 9016 ( ) RAL ........ Note: When fanlight opening systems are used on bottom-hung casements, we prescribe the use of separate safety scissors for product liability reasons. These represent an additional safety feature which guarantees the permanent connection of casement and frame, e.g. GEZE FPS |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE FPS gripping and cleaning scissors ( ) Size 1 from casement height 360 mm ( ) Size 2 from casement height 540 mm ( ) Size 3 from casement height 740 mm |

|  | Delivery and installation Wiring to be carried out on site by an electrical contractor according to the GEZE cable diagram. Delivery, installation and start-up to be carried out by plant fitters or service partner. Safety analysis is carried out, the operator receives instruction on how the system works and is handed the documentation. Maintenance and accident prevention inspection at least 1 x year according to GEZE specifications. |
| --- | --- |