|  | ......................... pcs. .............................. € .............................. € GEZE F 1200 cranked turn-and-tilt hardware Cranked turn-and-tilt hardware for convenient and simple operation of large and heavy aluminium windows. The hardware comprises a surface-mounted hinge side and a concealed central lock; this is operated via a crank gear. Operation opens the tilt opening width with variable adjustment. The number of horizontal/vertical centre locking systems depends on the closing force of the leaf. Hardware properties Can be used in aluminium profiles with the following hardware chamber dimensions: Leaf groove: 21 mm Frame groove: 14 mm Push rod groove depth: 6.5 mm Rebate space: 16 mm Application Leaf dimensions: ........ mm width (min. 750 mm – max. 2400 mm) ........ mm height (min. 750 mm – max. 3500 mm) Opening width with tilt opening: 180 mm Leaf weight: max. 200 kg (corresponding application diagram can be found in the installation drawing) Installation The crank gear can be installed both vertically and horizontally. Crank gear installation position: ( ) vertical / ( ) horizontal Hardware design Hinge side colour: ( ) EV1 / ( ) according to RAL Type of installation: ( ) DIN R / ( ) DIN L Operating element design Colour: ( ) EV1 / ( ) according to RAL Turn function: ( ) enabled (standard) ( ) mechanical turn block (key) Miscellaneous: ( ) removable crank handle ( ) extended crank gear |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Opening restriction, undampened or dampened Installing an opening restrictor allows the opening angle to be limited in the turning position. Choice of opening restrictors depending on leaf width. ( ) Size 0 (undampened) ( ) Size 1 (dampened) ( ) Size 2 (dampened) |
|  | ......................... pcs. .............................. € .............................. € GEZE Service package Compact Maintenance and testing of window systems (Optional position) Service package for maintenance and testing in accordance with ASR A1.6 and DIN 18232 2 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Check of the drive system fastening elements for a tight fit - Check functioning and condition of the drive system - Check the electrical connections of the drive system - Remove soiling from the drive system - Lubricate the hardware components with multi-purpose grease - Adjustment work - Free provision and updating of the test documents - Attachment of the inspection sticker - If safety-relevant defects are found, a repair proposal is generated - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Our service engineers are deployed within 24 hours of receipt of a report during our business hours from Mon.-Fri. 7.00 am - 5.00 pm - Special rates apply for interventions outside our business hours and for short response times within one day - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € GEZE Service Package Comfort Maintenance and testing of window systems (Optional position) Service package for maintenance and testing in accordance with ASR A1.6 and DIN 18232 2 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty from 12 to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - There is no charge for labour during the warranty period - One maintenance per contract year - Check of the drive system fastening elements for a tight fit - Check functioning and condition of the drive system - Check the electrical connections of the drive system - Remove soiling from the drive system - Lubricate the hardware components with multi-purpose grease - Adjustment work - Free provision and updating of the test documents - Attachment of the inspection sticker - On request, training for staff in how to operate the system - If safety-relevant defects are found, a repair proposal is generated. - Reduced hourly rates for repairs of interventions to eliminate faults. - No separate charging for faulty or worn wear & tear parts up to €25 per maintenance. - In the event of replacement of faulty or worn wear & tear parts in excess of €25, only the spare part is chargeable, with no separate charging for labour. - Our service engineers are deployed within 24 hours of receipt of a report during our business hours from Mon.-Fri. 7.00 am - 5.00 pm. - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Installation and functional test Installation and functional test only by an expert authorised by the manufacturer. |
|  | ......................... pcs. .............................. € .............................. € Delivery and installation Delivery, installation and commissioning through plant fitters or service partner. Safety analysis, instruction of the operator as to how the system works and handing over of the documentation. Annual maintenance and technical inspection by an expert authorised by the manufacturer incl. documentation of the inspection in a log book. |